## Slide 1
Geo-spatial Data for International Development Data, Methods and Concepts
Miranda Lv | GIS Analyst | zlv@aiddata.wm.edu
GCF Training
Jan 2019

## Slide 2
Topics
Vector & Raster Data
  Loading and visualizing maps
  GeoQuery data
  Zonal statistics analysis: mean, min, max
Geocoding
  Coding one given GCF project
Change monitoring
  Use of satellite remote sensing data to identify the state of land cover (NDVI)
  Before and after states for a given project regarding to vegetation index changes
  Land cover classifications
Spillover Analysis
  Estimation of spillover effects, eg: deforestation occurred in areas proximate to an area of project implementation
Overlap & Spatial Interpolation
  Creating an interpolated raster surface using sparse data, weather station, pollutant emission etc
Hotspot, cluster and population weighting
  Identify the hotspot of aid activities
  Spatial uncertainty (exact location of aid is not recorded)
Geospatial data for development (Thinking spatially and ask yourself what type of questions you want to answer)

## Slide 3
www.gcf.geoquery.org

## Slide 4
Spatial Data
Non-spatial data: information describing a certain set of elements.
  Eg: when describing African countries, non-stpatial data might include population, average income, number of hospitals, etc.
Spatial Data: adding new dimension to non-spatial data by specifying geographic location.
  Eg: above non-spatial info plus geographic location, and extent of each country

## Slide 5
Spatial data refer to the real-world geographic objects of interest, such as streets, buildings, lakes, and countries, and their respective locations. GIS software keeps track of both the spatial and attribute data and permits us to link the two types of data together to create information and facilitate analysis.
Source: https://saylordotorg.github.io/text_essentials-of-geographic-information-systems/s11-02-multiple-layer-analysis.html

## Slide 6
Spatial Data
- Vector
    Points
      Longitude and latitude
      Eg: buildings, trees, rain gauges
    Lines
      Two or more vertices
      Eg: streets, highways, rivers
    Polygons
      Enclosed areas
      Eg: administrative country boundaries, national parks, etc.

## Slide 7
Spatial Data
- Vector
    Attribute table:
      Text, numerical information that describe the features

## Slide 8
Spatial Data
- Vector
    Common vector file types:
      Shapefile. Designed by Environmental Systems Research Institute (ESRI) for use with its ArcGIS software, the shapefile (.shp) is arguably the most commonly-used file type for storing and sharing vector spatial data.
        .shp: shape format, saved the feature geometry
        .shx: shape index format, a positional index of the feature geometry to allow seeking forwards and backwards quickly
        .dfb: attribute format; columnar attributes for each shape
        .prj: projection format, the coordinate system and projection information
        Note: Include all above files types when you share your data with others.
      GeoJson: an open standard format designed for representing simple geographical features, along with their non-spatial attributes (.geojson)

## Slide 9
Spatial Data
- Raster
    Continuous:
      Eg: NDVI, nighttime light, soil quality, vegetation index, elevation, etc
    Discrete (categorical):
      Eg: landuse cover
    Common raster file type: .tiff

## Slide 10
QGIS
Load data
  Vector
  Raster
  Delimited text file: has coordinates
Attribute table
  Filter fields
  Select features and export the selected features;
Join attribute by location
  Joined GEF points to administrative level 1 boundaries and calculate the sum of aids to each state
Join attribute by id
  Download data from geoquery, which has ADMs boundary ids;
  Join the co-variables downloaded from geoquery to ADMs boundaries to be able to visualize environmental related co-variables;

## Slide 14
Geocoding
Geocoding: a process of transforming a description of a location, such as address or a name of a place, to geographic coordinates.
  Eg:
  Art Center Incheon ---> latitude: 37.3938409, longitude: 126.6273452

## Slide 15
Geocoding Improvements
Geocoding 2.0 - Richer, more precise data on activities
Original geocoding methods involved point base coding schemes with inherently limited spatial detail (e.g., project in town recorded as coordinates of town center and code which identified it as a populated place)
Now use true (or best approximation of) actual spatial features defining where investments went (e.g., project in town recorded as polygon drawn around town border)
Lines defining infrastructure development such as roads, power lines, irrigation networks
Polygons for land tenure, protected areas, etc.

## Slide 16
Updated methodology
  Old: point based with precision codes to describe location
  New: true geometry location definitions (lines, polygons)
Examples - bridges:
Geocoding Improvements
Geocoding Improvements

## Slide 18
Remote Sensing
Remote Sensing:
  Collection and interpretation of information about an object, area, or event from a distance;
  Sensor:
    Electromagnetic spectrum (EM) (frequency or the wavelength): continuous range of electromagnetic radiation
      X-ray (0.03-30 narometers), Ultraviolet radiation (0.03-0.4 micrometers), visible light (0.4-0.7 micrometers), infrared wavelengths, reflected infrared, etc.
    Detect the the emission and reflection of electromagnetic radiation from different objects.
    All objects have unique spectrum reflectance signatures;
    Eg: Fire (thermal band)

## Slide 19
Source: https://www.cbd.int/ts32/ts32-chap-3.shtml

## Slide 20
Source: http://www.physicalgeography.net/fundamentals/2e.html

## Slide 21
Spectral Reflection of Landcover
Source: http://www.geol-amu.org/notes/m1r-1-8.htm
Spectral Signature

## Slide 22
Download remote sensing data
https://mapshaper.org
https://earthexplorer.usgs.gov/

## Slide 23
Normalized Difference Vegetation Index
NDVI
  (NIR – Red)/(NIR + Red)
  A measure of the difference between near-infrared light and red light reflected from plants, and normalized by the sum of two wavelengths.
  Healthy plants has a higher value NDVI, absorb more red, and have a higher reflectance in the near-infrared.

## Slide 24
Source: https://katierosa.weebly.com/remote-sensing-change-analysis-and-land-cover-classifications.html

## Slide 25
Source: https://katierosa.weebly.com/remote-sensing-change-analysis-and-land-cover-classifications.html

## Slide 26
Source: https://katierosa.weebly.com/remote-sensing-change-analysis-and-land-cover-classifications.html

## Slide 27
Image Classification
Land Cover
  Materials at the ground, such as soil, vegetation, water, etc.
  Each pixel represents one material category
Classification
  Unsupervised classification:
    uses statistical distribution of the pixels within feature spaces exclusively to differentiate between classes
  Supervised classification
    Collect a subset of data for each object class as training dataset, these training dataset will be used in the classification algorithm to map the full image area

## Slide 28
Supervised classification
Definition of the land use and land cover classes (water, urban areas, buildings, forest, coniferous forest, deciduous forest, agriculture, etc)
Classification of training areas
  Training areas are collected from examine areas for each classes;
  Use the reflection data at each band to map the spectral signature;
Execution of the true classification algorithm
  Maximum likelihood (the classifier guesses the probability with which a specific pixel belongs to a specific class), minimum distance, etc
Verification, evaluation and inspection of the results

## Slide 32
Application
Monitoring the project implementation process
Wildlife conservation
Urban development

## Slide 33
Baseline NDVI trends
NDVI in 2010
NDVI in 2017
Monitoring

## Slide 36
Spatial interpolation
Spatial interpolation:
  Process with using points with known values to estimate value at other unknown points.
  Based on the assumption that sparsely distributed objects are spatially correlated.
  Eg: pollution, elevation, precipitation, etc. (statistical surface)
Source: https://docs.qgis.org/testing/en/docs/gentle_gis_introduction/spatial_analysis_interpolation.html

## Slide 37
Spatial Interpolation
Inverse Distance Weighting (IDW):
  Assumption: each input point has a local influence that diminishes with distance
  The closer points to the processing cell have greater weights than points further away.
  Weighting coefficient: assign to the sample points, it controls how the weighting influence will drop off as the distance from unknown point increases. The closer sample points to the unknown points have more influence to determine the value of unknown point.
Source: https://docs.qgis.org/testing/en/docs/gentle_gis_introduction/spatial_analysis_interpolation.html

## Slide 39
Spatial Interpolation
Triangulated Irregular Network (TIN)
  Used for high precision modeling of small areas, such as Digital elevation model (DEM)
  TIN results can have a higher resolution in areas where a surface is highly variable.
Source: https://docs.qgis.org/testing/en/docs/gentle_gis_introduction/spatial_analysis_interpolation.html

## Slide 42
Density Analysis
Kernel Density
  Calculate the density of features in a neighborhood around those features;
  Eg: Identify hotspot of aid activities for different donors; crime density in cities;
  Estimating the GCF aid allocation under condition of spatial uncertainty.

## Slide 44
Day 8, Jan 25